## Slide 1: The COSETI Observatory
Optical SETI Presentation 1
Overview
The Search for Extraterrestrial Intelligence in the Optical Spectrum
www.coseti.org
A collection of 120 slides that give an overview of the optical approach to SETI
Copyright ©, The Columbus Optical SETI Observatory, 1998

## Slide 2: The COSETI Observatory
Director, Dr. Stuart A. Kingsley
SMIEEE, MIEE, CEng.
Site of North America’s first visible SETI observatory dedicated to The Optical Search for Extraterrestrial Intelligence (OSETI) and the detection of pulsed and continuous wave interstellar laser beacons.
April 7, 1998
Version 1.1

## Slide 3: The COSETI Observatory
Stellar Nursery in M16
  7,000 light years from Earth
If it is too energy intensive to whiz around the galaxy is space-craft, and if faster than light communications are not possible, then the next best thing for communications between star systems is some form of free-space electromagnetic communications. Which form of electromagnetic interstellar communications technology is more likely to be used by ETIs is the subject of this scientific research activity.
The Electromagnetic Search for Extraterrestrial Intelligence (SETI)
  Microwave SETI
  Optical SETI

## Slide 4: The COSETI Observatory
The 100+ Mbyte Optical SETI Web Site Resource for Planet Earth.
www.coseti.org supports:
    RealAudio
    RealVideo
    RealPresenter
200 to 400 Billion Stars
  How can we be alone?
    100,000 light years in diameter.

## Slide 5: The COSETI Observatory
The Aim
  The aim of this first overview presentation is to assist others in writing about, teaching, otherwise promoting Optical SETI concepts, and constructing their own observatories.
  Detailed information on any topic may be obtained by browsing www.coseti.org .
Continuous wave beacon Optical SETI in the infrared was first suggested in 1961 by Nobel Laureate, Professor Charles H. Townes, inventor of the Maser. Pulsed beacon Optical SETI was first proposed by Dr. Monte Ross, noted photonics pioneer, a few years later. Monte Ross is presently in the process of setting up the Laser Museum Space Signal Observatory (LSSO) described later in this presentation.

## Slide 6: The COSETI Observatory
Contents
  Promotion of Optical SETI.
  The Drake Equation.
  The Electromagnetic Spectrum.
  Optical SETI Versus Microwave SETI.
  The Cyclops Report.
  Free-Space Laser Communications.
  Detecting Monochromatic Continuous Wave Laser Beacons.
  Professional Optical SETI.
  Adaptive Optics.
  Planetary Lasers.
  Detecting Extrasolar Planets.
  Detecting Pulsed Laser Beacons.
  Amateur Optical SETI.
  The COSETI Observatory.
  Retrospective Optical SETI.
  Laser Museum & Space Signal Observatory (LSSO).
  Optical SETI Conferences.
  SETIQuest.
  Summary.
  About Stuart Kingsley.
  Contact Information.
  Further Information.

## Slide 7: The COSETI Observatory
Three Types of Optical SETI.
  Professional.
    Large telescopes and sophisticated signal processing.
      Expensive.
  Amateur.
    Small telescopes and simple signal processing.
      Relatively inexpensive.
  Retrospective.
    A search through the historical record of stellar spectrographic plates.
      Inexpensive.
NGC1232

## Slide 8: The COSETI Observatory
The Electromagnetic Spectrum.
  The “Optical” spectrum regime covers the range of wavelengths from 10-3 m
  (far-infrared) to 10-8 m
  (ultra-violet).
SETI “Magic Optical Wavelengths”.
  Carbon Dioxide CO2
  (10.6 microns).
NGC5850

## Slide 9: The COSETI Observatory
What is the mission of The Columbus Optical SETI Observatory?
  To promote Optical SETI (OSETI) in the visible and infrared spectrums.
  To coordinate world-wide targeted OSETI searches.
  To conduct OSETI observations in the visible and near-infrared.
    For very short pulsed laser beacon signals.
    For continuous wave monochromatic beacons.

## Slide 10: The COSETI Observatory
Electromagnetic SETI on planet Earth today is really about the passive detection of attention-getting beacon signals that may be aimed in our direction by ETIs located in our sector of the Milky Way Galaxy.
Little consideration and attention has been given to the detection of wideband data channels that ETIs may also transmit, and which may be co-located with the beacon signals.
What really matters is the signal-to-noise ratio at the receiver - which may be maximized in a noisier region of the electromagnetic spectrum because that is where the gain of the antenna can be optimized. It is too simplistic to suggest that ETIs would choose the quietest region of the spectrum to send their signals.

## Slide 11: The COSETI Observatory
COSETI
9010-016

## Slide 12: The COSETI Observatory
Free-Space Laser Communications
  In the future, NASA will be using free-space laser communications for its deep space probes.
  Next century, the first HDTV pictures from our space probes sent to investigate the nearest stars will be transmitted by laser.
  Communications between geostationary satellites and low earth orbit satellites will also be supplemented by laser links.
  The future of communications is largely photonic, be it on the earth or between us and other stars!
Starfire Optical Range

## Slide 13: The COSETI Observatory
On a transmitter watt for watt basis, an interstellar free-space laser communications link can actually produce a higher signal-to-noise (SNR) than obtainable with a microwave link for distances greater than ten thousand light years.
Many microwave SETI researchers have implied that lasers are substantially inferior. This is NOT true.
200-inch Hale Palomar Telescope

## Slide 14: The COSETI Observatory
Search Strategy
  Targeted Star Search only.
    An “All Sky Survey” doesn’t make much sense at optical wavelengths as there are too many pixels to search in the celestial sphere.
  Look at the same stars that are the subject of the Microwave Targeted Search.
    1,000 solar-type stars out to a distance of about 100 light years.
Keck 2 Telescope

## Slide 15: The COSETI Observatory
COSETI
9010-023

## Slide 16: The COSETI Observatory
COSETI
9006-020

## Slide 17: The COSETI Observatory
COSETI
9308-001

## Slide 18: The COSETI Observatory
COSETI
9308-002

## Slide 19: The COSETI Observatory
COSETI
9306-003
System For Detecting Monochromatic Laser Beacon Signals

## Slide 20: The COSETI Observatory
COSETI

## Slide 21: The COSETI Observatory
COSETI
9512-001

## Slide 22: The COSETI Observatory
COSETI
9408-002

## Slide 23: The COSETI Observatory
COSETI
9512-002
System For Detecting Pulsed Laser Beacon Signals

## Slide 24: The COSETI Observatory
COSETI

## Slide 25: The COSETI Observatory
Stuart Kingsley
  10” Meade SCT located inside the 10 ft. diameter PRO-DOME (Technical Innovations, Inc.). Picture taken before an additional 1 ft. wall ring was added.
  SCT is shown on its equitorial mount though it is usually employed in its altazimuth configuration.
  Remember - “Small is Beautiful”.
COSETI

## Slide 26: The COSETI Observatory
RealPresenter/PowerPoint Presentations Planned:
  Overview.
  OSETI in Brief.
  Photo Gallery.
  Professional Optical SETI.
  Amateur Optical SETI.
  Retrospective Optical SETI.
  Heterodyne Detection.
  Direct Detection.
  Photon Counting.
  Observatory Data.
  Optical SETI for Young People.
Shuttle & HST